## Slide 1: Pre-Read Slides for NACA Workshop on Reduced-Complexity Models
NACA RCM Workshop
Kempton Park, South Africa
October 4, 2022

## Slide 2: Goals
Introduce some key concepts ahead of time for you to gain familiarity
Give enough information that you can look at and think about the simpler problems
Don’t worry: we will go over this all again during the workshop

## Slide 3: Impact Assessment
Air quality models are a way to ask “what if?” questions
Compare a present “baseline” to lower emissions under a control policy
Quantify changes in concentrations and health

## Slide 4: Impact Assessment
Maps of concentrations c(x,y)
Health outcomes
Economic and policy analysis

## Slide 5: RCMs: Really three different things…
Reduced-complexity model
(several different methods)
Marginal damages
(mortalities or $ per tonne emitted)
Source-receptor matrix
(how emissions at location X impact concentrations at location Y)
RCM developers
RCM users

## Slide 6: Air Pollution Impact Metrics
Think about the marginal damage caused by emitting one more tonne of a pollutant
Reminder: here we are just considering mortality from ambient PM2.5 (and precursors)

## Slide 7: RCMs Use #1: Assessing Damages
Using marginal damages becomes a relatively simple spreadsheet exercise for the user
Impacts of an emissions change, DE:
  (for all species, s and locations, l)

## Slide 8: Sample Calculation
What are damages associated with swine production in NC?
NEI2011 projected to 2017 / SCC 2805039000
(tons/yr)

## Slide 9: Spreadsheet Analysis
Emissions inventory
Marginal social damage (mortalities/tonne) from RCM
Mortalities caused by emissions in that county
= (marginal social damage)
x (emissions)
 |  |  | Total mortalities per year | 1331
County Name | County fips code | NH3 damages (mortalities/tonne) | Livestock NH3 emissions (tons/year) | Mortalities (per year)
Alamance | 37001 | 0.0118 | 0 | 0
Alexander | 37003 | 0.0107 | 1263 | 14
Alleghany | 37005 | 0.0088 | 0 | 0
Anson | 37007 | 0.0091 | 2959 | 27
Ashe | 37009 | 0.0091 | 0 | 0
Avery | 37011 | 0.0100 | 0 | 0
Beaufort | 37013 | 0.0062 | 807 | 5
Bertie | 37015 | 0.0075 | 1698 | 13
Total mortalities from emissions in all counties (sum of column)
…other counties (100 total)

## Slide 10: RCMs Use #2: Source-Receptor
If you want spatially resolved output, things are only slightly harder
Divide your country/region into locations:
  Regular Cartesian grid or municipalities
  Locations = (l1, l2, l3, … lN)
E.g. locations may be a list of countries*
  Locations = (Angola, Botswana, Eswatini, Lesotho, Malawi, Mozambique, Namibia, South Africa, Zambia, Zimbabwe)
  *short example: generally, RCMs are much higher resolution

## Slide 11: RCMs Use #2: Source-Receptor
Assume that we have emissions changes for each location … organize these values as a vector, :
We will generally want emissions vectors for each emitted species: , , , etc.

## Slide 12: RCMs Use #2: Mapping Changes
The resulting map of concentration changes can be calculated as:
…where is a vector of PM concentration changes with same locations in same order as emissions vector.
There are several “source-receptor” matrices,

## Slide 13: Source-Receptor Matrices
The source-receptor matrices, , map emissions changes into corresponding concentration changes
All of the important atmospheric behavior (transport, dispersion, chemistry, deposition) is embedded in the matrix values
Each RCM derives its S-R matrices differently (more later)
The source-receptor matrices are given to you
You just need to do the matrix-vector calculations
REACH-Southern Africa has 1781 locations (municipalities)
  Each S-R matrix is 1781 x 1781; and vectors have 1781 elements
Units: Emissions (tonnes/yr), concentrations (mg/m3), S-R (mg/m3 per tonne/yr)

## Slide 14: RCMs: Really three different things…
Reduced-complexity model
(several different methods)
Marginal damages
(mortalities or $ per tonne emitted)
Source-receptor matrix
(how emissions at location X impact concentrations at location Y)
RCM developers
RCM users
“Very easy”: ~1 hour with spreadsheet
“Moderately easy”: few hours in programming environment (R, Python, etc.)

## Slide 15: Concentration-Response Function
Premature mortality from chronic (annual-average) PM2.5 exposure
American Cancer Society (ACS) cohort
  6% increase in mortality per 10 mg m-3
Harvard 6-Cities
  14% increase in mortality per 10 mg m-3
Baseline mortality
Additional mortality
Concentration change
Relative risk

## Slide 16: Concentration-Response Function
Example calculation:
Hypothetical location
  Imagine a decrease in PM2.5 of -5 mg/m3 (=Dcx,y)
  Relative risk, R = 1.06 (ACS cohort)
  Population over 30 years old = 750,000 people
  Mortality rate = 9.4 deaths per 1,000 people
  Baseline mortality =

## Slide 17: Concentration-Response Function
Example calculation:

## Slide 18: Cost-Effectiveness Analysis
Idea: prioritize emissions reductions that bring most benefit for least cost
Needs:
  Number of lives saved (from RCM)
  Implementation cost of the policy ($)
The cost-effectiveness metric is the ratio:
Lower cost (per life saved) is better

## Slide 19: Conclusion
That was a very fast overview of key ideas about RCMs
Hopefully, that lets you:
  look at or try some of the simpler problems
  come to the workshop with foundational knowledge
Don’t worry: we will go over this all again
I am looking forward to meeting you all